## Slide 1: Andrew Ellis – Product Manager - Automation Phoenix Contact UK
Public

## Slide 2: Agenda
Introduction – Safety in Automation
1
The Situation for Manufacturers / Customers?
2
IO-Link
3
IO-Link Safety
4
What Happens Next
5
Further Information
6

## Slide 3: Introduction – Safety In Automation
Industrial Revolution
Electrical Revolution
Electronic Revolution

## Slide 4: Introduction – Safety In Automation
FSCP 12
FSCP 13
FSCP 14
FSCP 8
FSCP 18
Non-IEC
"C"
Non-IEC "A"
FSCP 6
FSCP 2
FSCP 1
FSCP 3
FSCP 17
IEC 61784-3-x: Collection of FSCPs (Functional Safety Communication Profiles)
Notes: Usually, IO-Link Safety will be a companion technology to upper level safety systems such as safety fieldbuses.
The safety communications of such fieldbuses is standardized within IEC 61784-3 series as FSCPs.
FSCP1: FF-SIS  Foundation Fieldbus Safety Instrumented Systems
FSCP2: CIP Safety  Ethernet IP (ODVA)
FSCP3: PROFIsafe  PROFINET, PROFIBUS (PNO)
FSCP6: Interbus Safety
FSCP8: CC-Link Safety
FSCP12: Functional Safety over EtherCat (FSoE)
FSCP13: Powerlink Safety
FSCP14: EPA Safety
FSCP17: RAPInet Safety
FSCP18: SafetyNet_p
NonIEC A: AS-i Safety at Work
NonIEC C: CANopen Safety

## Slide 5: The Situation for Manufacturers
Remote I/O with FS modules
Fieldbus & Functional Safety Communication Profile
More or less standardized interfaces
FSoE - Host
Cip Safety Scanner
PROFIsafe Controller

## Slide 6: The Situation for Customers
Machine builder decides on type of fieldbus to be used depending on deployment case
Thus, specific devices for each fieldbus with separate spares inventory, version maintenance and service are required
Thus, high degree of persistence to stay with "classic" interfaces such as OSSD, 4 to 20 mA, and etc. on "remote IO" field devices, since they are independent from fieldbus

## Slide 7: The Situation for Customers
However: no connection to Internet-of-Things (IoT) and Industry 4.0
Numerous new applications: (see "Smart Manufacturing") - New sensor technologies, e.g. strain, torque, pressure, multi-sensing, and etc. - More measuring sensors, e.g. object types, distance - Mechatronics, e.g. combinations sensors/actuators
Progressive miniaturization

## Slide 8: IO Link
How is this issue solved in automation?
  Standard Sensor / Actuator Communications profile independent of the fieldbus
  Point – Point Communication
  Standard IO support through hardware support
IO-Link

## Slide 9: IO Link -Standardisation
Standard Hardware configuration
  Power, IO, Communications
  Function Parameterised in IO-Link Master
IO-Link Sensor / Actuator
  Standard Connection
  Functionality / setup defined in a standardised IODD file for IO-Link Master software
  Setup of IO-Link device can be checked and stored in IO-Link master or controller.
1
2
4
3
5
1
2
4
3
5
I/Q
Power 1 power supply
Power 1 power supply
Power 2 extra power supply
P24 (Actuator)
N24 (Actuator)
C/Q
C/Q
Isolated from Power 1
Class A (Device)
1
2
3
4
Class B (Device)
1
2
3
4
5
M12-4
M12-5
Master
Master
Notes: Power supply and signal options:
Port Class A with Power 1 (maximum of 1000 mA @ IO-Link Safety!)
Port Class B with extra Power 2, depending on type of connector ≥ 3,5 A and wire gauges
Power 1 electrically isolated from Power 2
Port Class B shall be marked since pin layout is not compatible with Class A

## Slide 10: IO Link - Benefits
Benefits of IO-Link
New
Standard M12
On/Off-site Parameterization & Test (IODD)
One Sensor / Actuator device for World Market
Detection of Misconnection
Wiring & Power supply
(IO-Link)
COM + 24 V
Sensor / Actuator Replacement w/o Tools
Communication, bidirectional

## Slide 11: IO Link – Real World Benefits
More than 420 member
Companies worldwide

## Slide 12
Can this be extended to cover Safety?
Yes!

## Slide 13: IO Link
1
4
3
2
L-
I/Q
L+
SIO
COMx
4,8 / 38,4 / 230,4 kbit/s
C/Q
IO-Link communication
Switching signal ("SIO")
"Coded Switching"
Notes: Power and signals compliant with IEC 61131-2
Dual mode standard Devices: SIO (Standard Input Output) or IO-Link Communication (migration strategy)
SIO means traditional "switching signals"
IOL communication means "coded switching signals"
Three transmission rates: COM1 = 4,8; COM2 = 38,4; COM3 = 230,4 kbit/s
Pin layout corresponds to IEC 60947-5-2

## Slide 14: IO Link Safety
1
4
3
2
L-
I/Q
L+
IOL-OSSDe
COMx
4,8 / 38,4 / 230,4 kbit/s
C/Q
IOL-OSSDe: Equivalent signals
IOL-OSSDe
OSSD: Output Switching Sensing Devices (Solid state outputs)
OSSDe: = OSSD with equivalent switching signals; type C, class 1 according to Position Paper CB24I (ZVEI)
IO-Link Safety communication
OFF state
OFF state
Testpulses
Notes: Same as SIO and IO-Link communication
Pin layout corresponds to AIDA position paper
Safety: Dual mode FS-Devices: OSSDe (default) or IO-Link Safety communication
"e" stands for equivalent switching redundant signals
FS-Device output sends and reads back short test pulses for error detection
IO-Link Safety uses the I/Q signal line (Pin 2) for OSSDe operation (OSSD2e)
The German Car Manufacturers Association (AIDA) requires the same pin layout as IO-Link Safety.

## Slide 15: IO Link Safety To Fieldbus Level
PROFINET
Gateway: PROFINET IO-Link Integration ("Linking Modules")
PROFIsafe
Standardized Master Interface (SMI)
Configuration Manager
(Parameter) Data Storage
Acyclic Data Exchange
Diagnosis Unit
FS-IO mapping
IO-Link Safety (COM)
FS-DI (OSSDe)
Splitter/Composer
Cyclic Process Data Exchange
Master layers
PROFIsafe services + Protocol state machine
IO-Link Safety services + Protocol state machine
PROFIsafe ‒ IO-Link Safety Gateway
FS-Device
PROFIsafe
IO-Link Safety
PROFIsafe development kit
Notes: Safety integration is a linear extension of the fieldbus integration. Usually, there exist development kits for particular FSCPs such as PROFIsafe.
In case of SIL3 applications, these development kits recommend redundant microcontrollers to carry the FSCP protocol firmware.
IO-Link Safety fits well into this approach since it can be implemented totally hardware independent.
This figure shows also the "black channel" character of the FS-Master. The core part is a standard non-safety IO-Link Master with two modifications:
An FS-Master Port is able to sense the "READY" pulse of an FS-Device
An FS-Master is able to split the SPDU (safety protocol data unit) from the entire IO-Link message. In contrast, an FS-Master is able to compose an entire IO-Link message out of an SPDU and a non-safety data part.

## Slide 16: IO Link
How is this issue solved in automation?
  Standard Hardware Interface
  Standard Sensor / Actuator Communications profile independent of the fieldbus
  Point – Point Communication
  Standard IO support through hardware support
IO-Link

## Slide 17: IO Link Safety
Standard Safety Devices for next generation systems!
  Standard Safe Hardware Interface
  Standard Safety Communications profile independent of the fieldbus
  Point – Point Communication
  Safe IO support through hardware support
Safety Protocol
IO-Link Safety

## Slide 18: IO Link - Benefits
Benefits of IO-Link
Wiring & Power supply
(IO-Link)
New
Standard M12
On/Off-site Parameterization & Test (IODD)
Communication, bidirectional
One Sensor / Actuator device for World Market
Detection of Misconnection
COM + 24 V
Sensor / Actuator Replacement w/o Tools

## Slide 19: IO Link Safety - Benefits
Benefits of IO-Link
New
Standard M12 for Safe Devices
On/Off-site Parameterization & Test of Safe Devices (IODD) - PLe
One Safe device for World Market
Detection of Misconnection (Safe channels & Devices)
Wiring & Power supply
(IO-Link)
COM + 24 V
Safe Device Replacement w/o Tools
Safe Communication, bidirectional

## Slide 20: IO Link Safety - Summary
Remote I/O
0
7
0
7
0
7
Fieldbus with one of the FSCPs (IEC 61784-3)
0
6
DI
FS-Master
AI
OSSDe
or
COM
Switches
Analog
measure-
ments
Digitized
measure-
ments
Drives with safety
0
7
DO
Relays
0
7
AO
0 to 24 V
0 to 10 V
PM switching
IO-Link
Non safety
Device
4
7
Compact FS-Master (IP65)
0
3
IO-Link Safety
Low voltage switch
gear
Notes: Effect here is the same as with standard IO-Link. Instead of several different modules within a remote I/O such as FS-DI, FS-DO, FS-AI, and FS-AO, the user can focus on one FS-Master and save space, invest, and spares inventory .
Long lasting discussions for product managers about the number of channel types (how many FS-DI? FS-DO? FS-AI? Etc.) in compact devices can be alleviated  Just use a compact FS-Master with uniform Ports instead. They universally can be used for non-safety operation (DI, DO, COM) or safety operation (OSSDe, Safety COM).
Various different module interface technologies (OSSD, 0 to 10 V, 4 to 20 mA, etc.) become more and more obsolete.

## Slide 21: What Happens Next?
IO-Link Safety Standard is complete
First Workshop to certify the first IO-Link Safety Designers was run in May
Development and Test Tools are now available
Certification process has been formalised.
First Commerical IO-Link Safety Master and Devices to be demonstrated at end of 2023

## Slide 22: What Happens Next?

## Slide 23: Further Information
https://io-link.com/
https://www.profibus.com/
UNITED KINGDOM - uk.profibus.com
Also further information will be available through supporting Automation Vendors and Manufacturers

## Slide 24
Any Questions?